## Slide 1: Mobility management
mobility in computer network mean moving of a node from one network to another network
Spectrum of mobility:

## Slide 2: Terminologies in mobility
Home Network:
The home network is the permanent network to which the mobile node is associated.. The home network is responsible for managing the permanent address of the mobile node.
Example: Imagine your smartphone is configured to connect to your home Wi-Fi network. In this case, your home Wi-Fi network is the home network.
Permanent address:
Address in home mobile can always be used to reach to mobile
Ex:128.119.40.186

## Slide 3: Terminologies in mobility
Home agent :
The home agent is a network entity within the home network that performs mobility management functions on behalf of the mobile node. This includes tasks such as intercepting packets destined for the mobile node and forwarding them to its current location.

## Slide 4: Terminologies in mobility
foreign Network:
The foreign network is the network in which the mobile node is currently residing. This could be the network of a colleague or a different company when the mobile professional is on a business trip.
Care of address:
The address in visited network, you use until you are living in that place if you change the
location the care address also changes.

## Slide 5: Terminologies in mobility
Foreign Agent (FA):
The foreign agent is a network entity within the visited network that assists the mobile node with mobility management functions. It helps the mobile node register its current location and forwards data to it when needed.
Correspondent:
The correspondent is an entity that wishes to communicate with the mobile node.
This could be a server, another device, or any entity trying to establish communication
with the mobile node.

## Slide 6: Routing to a mobile node

## Slide 7: Important concepts
Home Network
A mobile node's home network is the network where it is permanently connected and has a permanent home address.
Home Agent
The home agent is a router on the home network that is responsible for keeping track of the mobile node's current location
Foreign Network
Foreign Agent

## Slide 8
A packet is sent to the mobile node's home address.
The home agent intercepts the packet and encapsulates it with the mobile node's current care-of address.
The encapsulated packet is sent to the foreign agent.
The foreign agent forwards the packet to the mobile node.

## Slide 9: Routing to a mobile node
Mobile Home Agent is like hotel

## Slide 10: Routing to a mobile node
Direct Routing
Indirect Routing

## Slide 11: Indirect routing
The correspondent sends a packet to the mobile node's home address.
The home agent intercepts the packet and looks up the mobile node's current location in its database.
The home agent encapsulates the packet with the mobile node's current care-of address.
The home agent forwards the encapsulated packet to the foreign agent.
The foreign agent decapsulates the packet and forwards it to the mobile node.
The mobile node receives the packet and processes it.

## Slide 12: Indirect routing
Cellular Networks
VPNs
CDNs
Caching

## Slide 13: Advantages and disadvantages of indirect routing
Reliable and secure routing mechanism
Efficient for mobile devices that move infrequently
No need for modifications to existing network infrastructure
Can introduce latency due to encapsulation and tunneling
May not be suitable for highly mobile devices
Requires coordination between home and foreign agents

## Slide 14: direct routing
The correspondent sends a packet to the mobile node's current care-of address.
The mobile node receives the packet and processes it

## Slide 15: Direct routing
Voice Video Call
Streaming
Apps
Gaming
Apps
AWS Connect
MS Team

## Slide 16: Advantages and disadvantages of direct routing
Faster and more efficient for highly mobile devices
Reduces latency compared to indirect routing
Suitable for real-time applications
Requires modifications to network infrastructure
May not be as secure as indirect routing
Can be more complex to implement and manage